## Slide 1: GPM: Leveraging Persistent Memory from a GPU
Shweta Pandey*, Aditya K Kamath*, Arkaprava Basu
https://csl.csa.iisc.ac.in/
* Both authors contributed equally
Notes: Csl website link
Github link where?

## Slide 2: Executive summary
Today, benefits of persistent memory (PM) limited only to CPU apps
We enable GPUs to harness PM without new hardware
We demonstrate three classes of GPU apps. that benefit from PM
We create a GPU runtime for easily writing recoverable GPU kernels

## Slide 3: Non-volatile memory (NVM) is here!
Byte-addressable Fine-grained persistence Near-DRAM performance
Persistent Memory (PM) = Byte-addressable NVM
Notes: No Bullet point, hz come up with byte-addressable, fine-grain persistence
Persistent Memory (PM) =

## Slide 4: Decade of PM research for CPU apps.
Notes: Use PM here. Don’t use NVM and PM interchangeably.
Persistent KVS + GPU-accelerated KVS : enabled when GPUs are able to perform fine-grained persistence
Pivot to gpKVS. Bring Figure 1 here itself. It brings huge throughput lift with exactly the same persistence guarantees from a pKVS.
We create a whole benchmark suite for these applications.

## Slide 5: GPUs can accelerate (some) PM apps.
Persistent KVS (pKVS)
[EuroSys’21, ATC ‘20, FAST’19]
GPU-accelerated KVS (gKVS)
[VLDB ’15, SoCC’15]
gpKVS: GPU-accelerated Persistent KVS
Notes: pKVS and gKVS and gpKVS
Use of persistent KVS and put the reference of motivation of importance of pKVS GPUs can accelerate the GET and SET operations on KVS like MegaKV
GPUs to accelerate GETs and SETs gpKVS -- can potentially

## Slide 6: Multi-fold speedup with gpKVS
Chart: 
| PmemKV | RocksDB-KVS | MatrixKV | GPM-KVS
Throughput (Kops/sec) | 764.182 | 646.391 | 353.955 | 2035.926
2.5
2.0
1.5
1.0
0.5
0
Throughput (Mops/s)
Notes: gpKVS instead of MegaKV + GPM
Multi-fold speedup with gpKVS – heading
Later we will discuss 3 categories of applications

## Slide 7: CPU Assisted Persistence (CAP)
PMem
DRAM
set(key, value)
cudaMemcpy(key)
cudaMemcpy(value)
persist(key, value)
PCIe
Notes: GPU kernel = GPU function
Animation – Push the fourth key value pair with the other three. Then move all four to the DRAM and then Pmem. Along with copy to device and persist appearing
Naïve way of doing it – CAP
Warp on GPU and single thread on CPU
CPU thread comes and guarantees persistence
Caches are volatile

## Slide 8: Our goal: in-kernel persistence
set(key, value)
persist(key, value)
PCIe
PMem
DRAM
Allow GPUs to directly store data on PM; enable fine-grained persistence
Notes: Guarantee persistence – horizontal line shows up saying persistence guaranteed
Box/Slide with benefits of persistence – GPU parallelism for persistence CPU software overheads ignored Direct access for loads and stores to PM

## Slide 9: Benefits of in-kernel persistence
Ease of programmability
Parallelism in persisting data
Selective persistence
Direct access to PM
1
2
3
4
Notes: Octagon or circle In-kernel persistence, and go to CPU
Ease of programming
Add parallelism data, wipe it, in the microbenchmark it is visible

## Slide 10: GPU with Persistent Memory: GPM
Create GPM with current hardware
Use cases for GPM: GPMBench
Runtime library for GPM: LibGPM
1
2
3
Notes: Remove the sub points
When the arrow comes
Sub points show up later with arrow
Create GPM with current hardware
IDEA slide

## Slide 11: GPM system model
PCIe
PMem
DRAM
SM
SM
SM
Core
LLC
MC
MC
DRAM
NVM
Interconnect
L2$ Bank 0
L2$ Bank N
GDDR
GDDR
IO Hub
CPU
GPU
PCIe
NVM is attached to the CPU, is accessed by GPU through PCIe

## Slide 12: Mapping NVM onto GPU address space
SM
SM
SM
Core
LLC
MC
MC
DRAM
NVM
Interconnect
L2$ Bank 0
L2$ Bank N
GDDR
GDDR
IO Hub
CPU
GPU
PCIe
Unified Virtual Address (UVA) space
GPU page table
Host Memory
Device Memory
Notes: Black boxes appear with animation of UVA
DRAM and NVM = host mem
GDDR = dev mem
System mem

## Slide 13: In-place updates to PM data structures
SM
SM
SM
SM
SM
Interconnect
L2$ Bank 0
L2$ Bank N
GDDR
GDDR
GPU
PCIe
set(key, value)
__threadfence_sys
SM
The system-scope threadfence pushes data from GPU to the CPU’s LLC
Core
LLC
MC
MC
DRAM
NVM
IO Hub
CPU
IO Hub
DDIO: Data Direct I/O
LLC
Notes: Barrier comes and stops at the LLC
As DDIO off, the barrier push the data to the NVM Bring it up in DDIO
Show the barrier moving
iMC = MC
No clflush instruction. We can use system scope threadfence. It will flush it out of the GPU memory.

## Slide 14: Guaranteeing persistence from GPU
IO Hub
LLC
MC
MC
DRAM
NVM
Interconnect
L2$ Bank 0
L2$ Bank N
GDDR
GDDR
CPU
GPU
PCIe
DDIO
set(key, value)
__threadfence_sys
Turn DDIO off to push the data to the persistent domain
Core
SM
SM
SM
SM
IO Hub
NVM
GPM achieved by
1. Mapping (parts of) NVM onto the GPU’s VA space with UVA. 2. Ordering data using system-scoped threadfence. 3. Guaranteeing persistence by selectively turning DDIO off.
Notes: Octagon for 1,2,3
Overlay with the three things
Show full form of DDIO on the right bottom side of slide
Go back to our proposal – Use cases of GPM: GPMBench
Gray out others
Runtime for GPM: LibGPM

## Slide 15: GPU with Persistent Memory: GPM
Create GPM with current hardware
Use cases for GPM: GPMBench
Runtime library for GPM: LibGPM
1
2
3
Notes: Create GPM with current hardware
IDEA slide

## Slide 16: GPMBench: Three application classes
Transactional | Long-running iterative | Native
gpKVS, GPU-accelerated DB | DNN, CFD, BLK, HS | BFS, SRAD, PS
Needs logging
Needs checkpointing
In-kernel persistence
Notes: GPU-accelerated pKVS GPU-accelerated DB on PM
Transactional needs logging, Long iterative needs checkpointing
Native does not need an explicit recovery, the recovery is in-kernel.
All of this is open-sourced

## Slide 17: GPU with Persistent Memory: GPM
Create GPM with current hardware
Use cases for GPM: GPMBench
Runtime library for GPM: LibGPM
1
2
3
Notes: Create GPM with current hardware
IDEA slide

## Slide 18: LibGPM: CUDA library for GPM
On an average only 19 lines of code changes are needed with libGPM
Logging | Checkpointing | Primitives
gpmlog_create_hcl, gpmlog_open, etc. | gpmcp_create, gpmcp_checkpoint, etc. | gpm_map, gpm_persist, etc.
Notes: Proposal slide again.
Flash the LibGPM table with its API.
Color code them one by one

## Slide 19: Conventional logging: single log
Shared log
T0
T1
T31
Thread data
. . .
Serialization while logging

## Slide 20: Conventional logging: distributed log
Distributed log
T0
T1
T31
Thread data
. . .
Not suitable for GPU’s parallelism
Notes: Due to poor data locality, the thread data is sent as multiple write operations
Not suitable for GPUs parallelism
Poor data locality, leading to multiple write operations

## Slide 21: HCL: Hierarchical Coalesced Logging
Shared log
Log structure reflects thread hierarchy
Threadblock 2
Threadblock 1
Threablocks
Warps
Warp
Threadblock
Grid
Notes: Have a backup slide for this Don’t put it here.

## Slide 22: HCL: Hierarchical Coalesced Logging
Shared log
T0
T1
T31
Thread data
. . .
Data split into 4-byte chunks
Notes: Have a backup slide for this Don’t put it here.

## Slide 23: HCL: Hierarchical Coalesced Logging
Shared log
T0
T1
T31
Thread data
. . .
Parallel logging GPU threads, coalesced writes to logs
Hardware coalescer
128-byte
cacheline
Notes: Idea bulb!
HW coalescer diff color
Parallel logging by GPU threads
Push everything to left and bring up the line graph or both or apps in a box
Move the first blocks from T0, T1.. T32 a little down Then there is HW coalescer that mashes them
And then the cacheline is moved to shared log. The cache line is marked using a thick line. Put a dotted line across it and call it 128B.

## Slide 24: HCL speeds up logging
Chart: Number of GPU threads
Upto 3x speedup over conventional logging!
Notes: Remove right side picture and
Idea bulb!
HW coalescer diff color
Parallel logging by GPU threads
Push everything to left and bring up the line graph or both or apps in a box
Move the first blocks from T0, T1.. T32 a little down Then there is HW coalescer that mashes them
And then the cacheline is moved to shared log. The cache line is marked using a thick line. Put a dotted line across it and call it 128B.

## Slide 25: Evaluation platform
CPU | 4 x Intel Xeon Gold 6242 (4 x 16 cores) @ 2.80GHz
GPU | NVIDIA Titan RTX (72 SMs, 24 GB GDDR6)
DRAM | 768 GB DDR4 @ 2933 MHz
NVM | 8 x 128 GB Intel Optane NVDIMM
Interconnect | PCIe 3.0 x 16
Software | Ubuntu 20.04, CUDA 11, PMDK 1.8, ext4-DAX
Notes: No simulation

## Slide 26: GPU accelerated PM applications
Type
Type
Type | Code | Evaluated applications
Transactional | gpKVS | Key-value store
 | gpDB | GPU-accelerated DB
Checkpointing | DNN | DNN training
 | CFD | Computational fluid dynamics
 | BLK | Black-Scholes
 | HS | Hotspot
Native | BFS | Breadth-first search
 | SRAD | Speckle reducing anisotropic diffusion
 | PS | Prefix sum
Notes: Font color and font size
GPU-accelerated PM application
Speaking – GPMBench apps are used
What is the cost for persisting data?

## Slide 27: Performance evaluation: CAP vs GPM
Chart: Speedup over CAP
| gpKVS | gpDB | DNN | CFD | BLK | HS | BFS | SRAD | PS
GPM | 8.227 | 5.2615 | 15.998 | 17.258 | 11.003 | 17.96 | 84.697 | 5.988 | 5.025
85
Notes: We compared against our baseline – cap. On an avg x perf benefit
BFS improves so much
gpKVS or gpDB
And where and how the benefits are coming from.
Much more evaluation in the paper

## Slide 28: Intel’s upcoming extended ADR (eADR)
SM
SM
Interconnect
L2$ Bank 0
L2$ Bank N
GDDR
GDDR
GPU
PCIe
SM
Core
LLC
MC
MC
DRAM
NVM
IO Hub
CPU
Persistence is guaranteed as soon as data reaches the caches
IO Hub

## Slide 29: CAP under eADR
SM
SM
Interconnect
L2$ Bank 0
L2$ Bank N
GDDR
GDDR
GPU
PCIe
SM
Core
LLC
MC
MC
DRAM
NVM
IO Hub
CPU
cudaMemcpy(key)
cudaMemcpy(value)
flush(key, value)
drain()
No need to flush the caches
IO Hub
set(key, value)

## Slide 30: GPM under eADR
SM
SM
Interconnect
L2$ Bank 0
L2$ Bank N
GDDR
GDDR
GPU
PCIe
set(key, value)
__threadfence_sys
SM
Core
LLC
MC
MC
DRAM
NVM
IO Hub
CPU
IO Hub
DDIO
No need to disable DDIO

## Slide 31: CAP and GPM with e-ADR (projection)
Chart: Speedup over CAP
| gpKVS | gpDB | DNN | CFD | BLK | HS | BFS | SRAD | PS
CAP-eADR | 1.9873 | 1.5328 | 1.8232 | 1.5182 | 1.5786 | 1.9185 | 1.2006 | 1.6432 | 1.2996
GPM-eADR | 110.5757 | 6.8069 | 18.4087 | 18.5987 | 10.6422 | 17.3354 | 142.7774 | 7.8754 | 14.4544
142
110
Notes: There is a lot more evaluation.
Cost of persistence?

## Slide 32: Summary
Our contributions:
Create GPM with in-kernel, fine-grained persistence in current hardware.
Show the importance of PM for GPU apps with a benchmark suite GPMBench.
Build a GPM runtime, libGPM, allowing programmers to easily use GPM.
GPUs can make use of persistence that NVMs provide.
We propose GPM to allow GPUs to leverage PM persistence.
Reproducible artifact: https://github.com/csl-iisc/GPM-ASPLOS22
1
2
3
Notes: To summarize, concurrency bugs threaten GPU applications. Newly evolving programming features also come with the possibility of new bugs.
To combat these bugs, we propose iGUARD, a race detector with relatively low overhead that requires no hardware changes and supports advanced synchronization.